## Slide 1
◉
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION FOR COOPERATIVE NOMA NETWORK
Adaptive helper selection and transmission-power decisions for cooperative NOMA
Course: Machine Learning (25SC2107E) | A.Y. 2026–27
Department: Electronics & Communication Engineering
Guide: Mr. N Lava Prasad, Assistant Professor, ECE
PROJECT TEAM
G. Harshith — 2520040079 V. Shivadarahas — 2520040038 B. Pavan — 2520040102
Koneru Lakshmaiah Education Foundation | A.Y. 2026–27

## Slide 2
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Presentation Outline
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
2
1
Problem Statement & Motivation
Changing wireless channels, interference and inefficient fixed resource allocation.
2
Objectives & Evaluation Metrics
Improve throughput, link reliability and energy efficiency.
3
Proposed Approach & Tools
Two PPO agents for relay selection and power allocation.
4
Simulation Dataset & Environment
Synthetic wireless states, fading, noise and candidate relays.
5
Training & Comparative Results
Evaluate trained PPO against random and fixed/heuristic baselines.
6
Conclusion & Future Work
Limitations, realistic channel models and larger cooperative networks.

## Slide 3
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Problem Statement & Motivation
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
3
CHALLENGES IN COOPERATIVE NOMA
Wireless channel quality changes with fading, distance and interference.
A weak or far user may receive an unreliable direct signal.
Choosing a suitable helper relay requires comparing multiple channel links.
Power allocation must balance the weak user's reliability and the strong user's data rate.
Fixed relay and power rules may not adapt to changing network conditions.
CORE RESEARCH QUESTION
Can Multi-Agent PPO learn to select a suitable relay and allocate transmission power using current network conditions?

## Slide 4
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Project Objectives & Evaluation Metrics
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
4
Improve Throughput
Increase the sum of achievable rates for the two NOMA users.
Select a Useful Relay
Choose a candidate helper based on its simulated channel links.
Allocate Power Adaptively
Select a power split that supports the weak user while serving the strong user.
Measure Reliability
Track SINR, outage probability and approximate BER.
CORE METRICS: Throughput | SINR | Outage Probability | Approx. BER | Energy Efficiency | Power Consumption

## Slide 5
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Proposed Methodology & System Workflow
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
5
1
Generate State
Simulate channel gains, noise, interference and distances.
2
Observe
Both PPO agents receive a normalized network-state vector.
3
Select Relay
Relay agent selects one of three candidate helpers.
4
Allocate Power
Power agent selects a discrete weak-user power fraction.
5
Evaluate & Learn
Shared reward uses sum rate, energy efficiency and outage.
Loop: Observe network → Choose helper relay → Select power split → Calculate reward and metrics → Update PPO policies

## Slide 6
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Software Stack & Technical Tools
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
6
Python
Environment, training loop, evaluation and data generation
Core development
NumPy & Pandas
Numerical channel simulation, data tables and metrics
Data and calculations
PyTorch
Actor–critic neural networks and PPO updates
Reinforcement learning
Matplotlib
Training curves, EDA plots and baseline comparisons
Visual analytics
Google Colab / Jupyter
Interactive execution and experiments
Experiment platform

## Slide 7
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Synthetic Wireless Dataset & State Features
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
7
2,500
Synthetic samples
3
Candidate relays
2
NOMA users
10 units
Fixed total power
FEATURES INCLUDED
Direct channel gains for weak and strong users
Base-station-to-relay and relay-to-weak-user gains
Interference and noise power
Relay choice and power split
SINR, rates, throughput, outage, BER proxy and reward
DATASET NOTE
The CSV is generated by the project's simulator with randomized actions. It is synthetic educational data, not a measured dataset from a live 5G/6G network.

## Slide 8
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Cooperative NOMA Network Model
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
8
Base Station
Helper Relay
Weak User
Strong User
Illustrative links; the simulator uses simplified channel-gain equations.
MODEL ASSUMPTIONS
Rayleigh-like fading and distance-based path loss
Additive noise and a simple interference term
Weak user benefits from a simplified two-hop relay link
Strong user is assumed to use ideal SIC
Rates are calculated using log₂(1 + SINR)

## Slide 9
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Simulation Environment: State, Actions & Reward
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
9
Observation / State
Direct user channel gains
Candidate relay channel gains
Interference level
Noise level
Log-scaled normalized features
Agent Actions
Relay agent: choose relay 0, 1 or 2
Power agent: choose a fraction from 0.55 to 0.90 for the weak user
Remaining power is allocated to the strong user
Total power remains fixed
Shared Reward
Reward = sum rate + 0.15 × energy efficiency − 1.5 × outage
Encourages higher rate
Rewards energy efficiency
Penalizes an outage event

## Slide 10
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
PPO Objective & Reward Design
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
10
R = (Rateweak + Ratestrong) + 0.15 × EnergyEfficiency − 1.5 × Outage
Throughput
Sum of the two users' simplified achievable rates.
Energy Efficiency
Sum rate divided by the fixed normalized power budget.
Outage Penalty
Penalty applies if either user's rate falls below the configured threshold.
Reward coefficients are design choices for this educational simulation and should be tested for sensitivity.

## Slide 11
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Baseline Methods for Comparison
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
11
Random
Randomly selects a relay and a power split.
Fixed Relay
Always selects relay 0 and uses a 0.70 weak-user power fraction.
Conventional Heuristic
Chooses the relay with the strongest estimated relay-assisted link and a channel-aware power split.
PPO Agents
Uses the trained relay and power policies to make state-dependent decisions.

## Slide 12
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
PPO Agent Training Setup
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
12
Algorithm
Clipped Proximal Policy Optimization
Policy architecture
Actor–critic MLP, 64 × 64 hidden layers
Optimizer
Adam
Learning rate
3 × 10⁻⁴
Clip range
0.20
Update epochs
5 per collected batch
Training episodes
Configurable; default 300
Agents
Separate relay-selection and power-allocation PPO agents

## Slide 13
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Training Progress & Reward Curve
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
13
GENERATE THIS GRAPH FROM YOUR ACTUAL RUN
Run src/train_evaluate.py. The script saves results/training_reward.png and results/training_log.csv. Insert the resulting graph here after training.
WHAT TO CHECK
Does the rolling reward improve?
Does reward stabilize?
Are outage and BER reduced?
Compare against the baselines
Use your measured output only

## Slide 14
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Evaluation Metrics & Interpretation
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
14
Throughput
Sum of weak-user and strong-user achievable rates.
SINR
Signal power relative to interference and noise.
Outage Probability
Fraction of evaluated samples below a rate threshold.
Approx. BER
Simplified BPSK-style error proxy; not a coded PHY result.
Energy Efficiency
Throughput per normalized unit of transmit power.
Power Consumption
Fixed budget in this version; therefore not a varying outcome.

## Slide 15
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Comparative Analysis: PPO vs Baselines
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
15
RESULTS TABLE AND BAR CHARTS ARE GENERATED AFTER TRAINING
Use results/baseline_summary.csv and results/comparison_throughput.png, comparison_outage.png, comparison_energy_efficiency.png and comparison_ber.png after running the evaluation script.
FAIR COMPARISON
Evaluate every method on the same simulator assumptions
Use the same evaluation sample count
Report average metrics
Do not assume PPO wins before checking output

## Slide 16
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
How to Read the Results
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
16
If throughput rises
The selected relay and power split may be improving aggregate data rate.
If outage falls
More evaluated states meet the minimum-rate condition.
If BER proxy falls
The simulated links have stronger SINR under the approximate model.
If PPO underperforms
Increase training, test seeds, inspect reward scaling and compare the state/action design.

## Slide 17
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
End-to-End System Architecture
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
17
Network State
Channel gains, noise, interference
→
Relay PPO
Choose candidate helper
→
Power PPO
Choose weak-user power fraction
→
NOMA Simulator
Calculate SINR, rates and outage
→
Shared Reward
Update both policies
The environment returns a new randomized network state each step; each decision is evaluated with a shared reward.

## Slide 18
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Limitations & Future Enhancements
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
18
CURRENT LIMITATIONS
Simplified channel and relay-link equations
One-step episodes and independent PPO policies
Fixed total transmit power
Approximate BER and ideal SIC assumptions
Synthetic data, not field measurements
FUTURE WORK
Add realistic Rayleigh/Rician and mobility models
Use continuous power allocation
Test more users and relay candidates
Use multi-seed statistical evaluation
Explore centralized training with decentralized execution

## Slide 19
MACHINE LEARNING (25SC2107E) | DEPARTMENT OF ECE
Project Conclusion & Research Summary
MULTI-AGENT PPO-BASED RELAY SELECTION AND POWER ALLOCATION | Dept. of ECE
19
1. Joint Resource Decisions
Relay selection and power allocation are modeled as two PPO decision tasks.
2. Adaptive Learning
The agents learn from simulator feedback rather than using only fixed rules.
3. Quantitative Evaluation
Throughput, SINR, outage, approximate BER and energy efficiency are recorded.
4. Reproducible Foundation
The code can be extended with richer channels, mobility and more users.

## Slide 20
Thank You!
Questions & Open Discussion
Project: Multi-Agent PPO-Based Relay Selection and Power Allocation
Course: Machine Learning (25SC2107E) | A.Y. 2026–27
Guide: Mr. N Lava Prasad | Department of ECE
G. Harshith • V. Shivadarahas • B. Pavan